TRC3500 – Project One – Customer Requirements

Requirement	Completed
Microprocessor used to power up the circuit through 5 V USB
Microprocessor is used to drive the whole circuit
Ultrasonic receiver/transmitter is used
Must work up to 3500 mm / 35.00 cm
Must have accuracy of ∓ 3 mm
Must use a 7 segment, 4 digit display
Must be able to display information in both Imperial and Metric system
Must have a mechanism to switch between Imperial and Metric system
Must indicate the unit system with an LED
Must store the current unit system in EEPROM
Must store unique identification number in EEPROM (Group Number)
Display Update must be accomplished using software
When the switch is pushed, a 200 mS beep must be heard

Operational Requirements
Up on powering up, the sleep mode is entered
Up on press of a button (either quick push or held down), the sleep mode is measured
The measurement is made
The distance is displayed on the 7 segement display
The display stays on for 2 seconds
The device is returned back to the sleep mode

*Sleep mode is defined as having a blank screen, with only 1 (one) decimal point flashing at the rate of 1 Hz